SECTION 09 2526

ONE-COAT STUCCO

This section includes editing notes to assist the user in editing the section to suit project requirements. These notes are included as hidden text, and can be revealed or hidden by one of the following methods:

Microsoft Word 2007: Click the Office button, select Word Options, select Display, then select or deselect the HIDDEN TEXT option.

Microsoft Word (earlier versions): From the pull-down menus select TOOLS, then OPTIONS. Under the tab labeled VIEW, select or deselect the HIDDEN TEXT option.

Corel WordPerfect: From the pull-down menus select VIEW, then select or deselect the HIDDEN TEXT option.

This master specification section has been prepared by EZ Wall Premix for use in the preparation of a project specification section covering EZ Wall premixed, Portland cement based stucco base coat with either Portland cement, acrylic, or elastomeric finish coat, commonly referred to as “one coat” stucco. One coat stucco may be applied directly to concrete or masonry surfaces, or over sheathing and metal lath or wire mesh.

This specification is a part of the SpexPlus system, which comprises a full architectural master specification that can be used to specify all project requirements.

The following should be noted in using this specification:

Hypertext links to specific websites are included after names of organizations whose standards are referenced within the text, to assist in product selection and further research. Hypertext links are contained in parenthesis and shown in blue, e.g.:

(www.nocsa.org)

Optional text requiring a selection by the user is enclosed within brackets, e.g.: "Section [09 0000.] [_____.]"

Items requiring user input are enclosed within brackets, e.g.: "Section [_____ - ________]."

Optional paragraphs are separated by an "OR" statement, e.g.:

**** OR ****

Sustainable requirements are included for projects requiring LEED certification, and are included as green text. For additional information on LEED, visit the U.S. Green Building Council website at www.usgbc.org.

For assistance on the use of the products in this section, contact EZ Wall Premix at 214-928-7748, by email at info@ezwallpremix.com, or visit their website at http://www.dynamicclosures.comWww.ezwallpremix.com.http://www.ezwallpremix.commailto:info@nocsa.org,http://www.nocsa.org

For assistance with obtaining or using the SpexPlus Master Specification System contact SpexPlus by calling 1-888-877-SPEX (1-888-877-7739), by email at chaney@spexplus.net, or visit our website at www.spexplus.net.

PART 1	 - GENERAL

1.1	SUMMARY

Edit the following paragraphs to include only those items specified in this section.

A.	Section Includes:

1.	Premixed, Portland cement based stucco base coat and finish coat.

2.	Metal lath.

3.	Metal trim and accessories.

4.	Polystyrene foam [details.] [insulation.]

Coordinate the following paragraphs with other sections in the project manual.

B.	Related Sections:

1.	Division 01: Administrative, procedural, and temporary work requirements.

2.	Section [03 3000 - Cast-In-Place Concrete:] [__ ____ - _______:] Concrete substrate to receive stucco system.

3.	Section [04 2000 - Unit Masonry:] [__ ____ - _______:] Masonry substrate to receive stucco system.

4.	Section [06 1100 - Framing and Sheathing:] [__ ____ - _______:] [Plywood] [Oriented strand board sheathing] substrate to receive stucco system.

5.	Section [06 1643 - Gypsum Sheathing:] [__ ____ - _______:] Gypsum sheathing to receive stucco system.

6.	Section [07 2800 - Moisture Barriers:] [__ ____ - _______:] Weather-resistant wall barrier.

7.	Section [07 6200 - Sheet Metal Flashings and Trim:] [__ ____ - _______:] Metal wall flashings.

8.	Section [07 6500 - Flexible Flashings:] [__ ____ - _______:] Flexible wall flashings.

9.	Section [07 9200 - Joint Sealers:] [__ ____ - _______:] Joint sealers used in conjunction with stucco system.

10.	Section [09 2236 - Lath:] [__ ____ - _____:] [Metal lath.] [Wire mesh.]

1.2	REFERENCES

In the following paragraphs, retain only those reference standards that are used elsewhere in this section.

A.	ASTM International (ASTM) (www.astm.org):

1.	C144 - Standard Specification for Aggregate for Masonry Mortar.

2.	C847 - Standard Specification for Metal Lath.

3.	C897 - Standard Specification for Aggregates for Job-Mixed Portland Cement-Based Plasters.

4.	C926 - Standard Practice for Application of Portland Cement-Based Plaster.

5.	C932 - Standard Specification for Surface-Applied Bonding Compounds for Exterior Plastering.

6.	C1063 - Standard Specification for Installation of Lathing and Furring to Receive Interior and Exterior Portland Cement-Based Plaster.

B.	National One Coat Stucco Association (NOCSA) (www.nocsa.org).

1.3	SUBMITTALS

Limiting submittals to only those actually required helps to minimize liability arising from the review of submittals. Minimize submittals on smaller, less complex projects.

Include the following for submission of product data and samples for the Architect's review.

A.	Submittals for Review:

1.	Product Data: Manufacturer’s technical information and application instructions.

2.	Samples:

a.	[6 x 6] [__ x __] inch finish coat samples showing available colors.

b.	[After color selection, submit] [12 x 12] [__ x __] inch plaster samples showing finish coat in [specified] [selected] color and texture.

c.	[6] [__] inch long trim samples.

d.	12 x 12 inch metal lath samples.

Include the following for submission of sustainable design submittals.

B.	Sustainable Design Submittals:

1.	Recycled Content: Certify percentages of post-consumer and pre-consumer recycled content.

2.	Regional Materials: Certify distance between manufacturer and Project and between manufacturer and extraction or harvest point in miles.

C.	Quality Control Submittals:

1.	Building Code Acceptance: Copies of current manufacturer’s evaluation reports issued by Code authorities showing acceptance of stucco system.

2.	Copy of stucco manufacturer’s current NOCSA membership certificate.

1.4	QUALITY ASSURANCE

The following paragraph specifies a minimum level of experience required of the parties performing the work of this section. Retain if required, and edit to suit project requirements.

A.	Installer Qualifications: Minimum [2] [__] years [documented] experience in work of this Section.

Include the following for full size mockups for review of construction and coordination of work of several sections.

B.	Mockup:

1.	Size: Minimum [4 x 4] [__ x __] feet.

2.	Show: Plaster color and texture, trim, and overall workmanship.

3.	Locate [where directed.] [____.]

4.	Approved mockup may [not] remain as part of the Work.

C.	Not Acceptable: Lines in stucco caused by variations in application or finishing techniques, cold joints, and other surface defects visible when viewed from a distance of 10 feet.

1.5	DELIVERY, STORAGE AND HANDLING

A.	Deliver materials in manufacturer’s original, unopened contains bearing identifying labels.

B.	Store materials off ground or floor, properly covered.

C.	Protect cement from moisture and humidity changes.

D.	If water-based materials are used, protect from freezing.

1.6	PROJECT CONDITIONS

A.	Cold Weather Requirements: Do not apply stucco unless minimum ambient temperature is forecast to be above 40 degrees F during and for minimum 24 hours after application.

B.	Hot Weather Requirements: Protect applied stucco from uneven and rapid evaporation during hot, dry, or windy weather by fogging surface with potable water.

PART 2	 - PRODUCTS

2.1	MANUFACTURERS

A.	Contract Documents are based on products by EZ Wall Premix, Inc. (www.ezwallpremix.com)

Edit the following to indicate whether or not substitutions will be permitted for the products in this section.

B.	Substitutions: [Under provisions of Division 01.] [Not permitted.]

2.2	MATERIALS

Include the following for non-sanded, fiber-reinforced base coat requiring the addition of sand and water at the project site.

A.	Base Coat:

1.	Description: Fiber-reinforced, stucco concentrate consisting of Portland cement, chopped glass fibers, and proprietary additives.

2.	Source: [EZ Concentrate.] [EZ Scratch and Brown w/fiber.]

**** OR ****

Include the following for non-sanded, non-fiber-reinforced base coat requiring the addition of sand and water at the project site.

B.	Base Coat:

1.	Description: Concentrate consisting of Portland cement, chopped glass fibers, and proprietary additives.

2.	Source: [EZ Spread.]

Include the following for a Portland cement finish coat; edit to suit project requirements.

C.	Finish Coat:

1.	Type: Cement based colored stucco finish coat consisting of Portland cement, lime, graded aggregate, colorant, and proprietary ingredients.

2.	Color: [[Custom] [____] color.] [Color to be selected from manufacturer’s full color range.]

3.	Color-stabilizing spray: Fog coat in color to match finish coat, consisting of Portland cement, lime, graded aggregate, colorant, and proprietary ingredients.

**** OR ****

Include the following for an acrylic finish coat with aggregate; edit to suit project requirements.

D.	Finish Coat:

1.	Primer: Acrylic based consisting of acrylic polymers and proprietary ingredients.

2.	Finish coat: Tinted acrylic finish with aggregate consisting of acrylic polymers, graded aggregate, colorant, and proprietary ingredients.

3.	Color: [[Custom] [____] color.] [Color to be selected from manufacturer’s full color range.]

**** OR ****

Include the following for an elastomeric finish coat with aggregate; edit to suit project requirements.

E.	Finish Coat:

1.	Primer: Acrylic based consisting of acrylic polymers and proprietary ingredients.

2.	Finish coat: Tinted elastomeric finish with aggregate consisting of polymers, graded aggregate, colorant, and proprietary ingredients.

3.	Color: [[Custom] [____] color.] [Color to be selected from manufacturer’s full color range.]

**** OR ****

Include the following for a non-sanded acrylic finish coat; edit to suit project requirements.

F.	Finish Coat:

1.	Primer: Acrylic based consisting of acrylic polymers and proprietary ingredients.

2.	Finish coat: Tinted acrylic finish consisting of 100 percent acrylic polymers and proprietary ingredients.

3.	Color: [[Custom] [____] color.] [Color to be selected from manufacturer’s full color range.]

**** OR ****

Include the following for a non-sanded elastomeric finish coat; edit to suit project requirements.

G.	Finish Coat:

1.	Primer: Acrylic based consisting of acrylic polymers and proprietary ingredients.

2.	Finish coat: Tinted elastomeric acrylic finish consisting of 100 percent acrylic polymers and proprietary ingredients.

3.	Color: [[Custom] [____] color.] [Color to be selected from manufacturer’s full color range.]

H.	Sand: ASTM C897, natural or manufactured, uniformly graded, washed.

I.	Water: Potable.

J.	Metal Lath: ASTM C847, expanded self-furring diamond mesh, galvanized.

Include the following for decorative details; indicate sizes and shapes on Drawings. Polystyrene foam may be applied over sheathing, concrete, or CMU substrates to form quoins, bands, etc., may be applied over larger areas to produce reveals and additional thickness, or may be used for additional insulation value. When used as sheathing, polystyrene must conform to Evaluation Report requirements for density, thickness, and edge details. Polystyrene used in noncombustible construction must conform to Evaluation Report requirements.

K.	Polystyrene Insulation:

1.	Expanded or extruded polystyrene, minimum 0.9 PCF density, of sizes and shapes indicated on Drawings.

2.	Adhesive: Type recommended by insulation manufacturer; compatible with substrate materials.

Edit the following to include only those metal trim profiles required for project.

L.	Metal Accessories:

1.	Material: Zinc-coated steel, zinc alloy, or PVC; thickness to suit stucco thickness.

2.	Corner bead: General purpose type, with expanded or perforated flanges, or corner reinforcement.

Edit the following to include desired casing bead profile.

3.	Casing bead: [Square] [Rounded] profile, expanded or flanged to suit project conditions.

4.	Control joint: Accordion profile with 1/4 inch slot.

5.	Expansion joint: Adjustable type, free-floating, with adjustment from 1/4 to 5/8 inch.

6.	Weep screed: Perforated for drainage.

2.3	ACCESSORIES

Edit the following to suit project requirements.

A.	Fasteners:

1.	Type and size suited to application, hot-dip galvanized steel.

2.	[Concrete] [Masonry] backup: Minimum 1/2 inch penetration.

3.	Metal stud backup: Meet ASTM C1063.

B.	Tie Wire: 16 gage, galvanized steel, soft annealed.

Include the following for stucco applied directly to concrete or masonry substrate.

C.	Bonding Agent: ASTM C932; type recommended for bonding plaster directly to [concrete] [masonry] surfaces.

2.4	MIXING

A.	Mix materials in accordance with manufacturer’s instructions.

B.	Use mechanical mixer; hand mixing not permitted unless authorized in advance by Architect.

C.	Accurately proportion materials for initial mixture using measuring devices of known volume.

D.	Withhold 10 percent of water until mixing is nearly complete, then add remainder as required to achieve workable mix.

E.	Maintain mixer in continuous operation while adding materials.

F.	Mixtures may be retempered one time after initial mixing.

G.	Discard frozen, caked, and hardened mixes. Discard mixes not used within 60 minutes after initial mixing.

PART 3	 - EXECUTION

3.1	PREPARATION

Include the following two paragraphs for stucco applied directly to concrete or masonry substrate.

A.	Clean substrate surfaces of oil, [release agents,] other deleterious materials, and loose and foreign matter.

B.	[Wet high suction bases with fine water spray to produce uniformly damp surface.]

C.	[Apply bonding agent in accordance with manufacturer's instructions.]

Include the following three paragraphs for stucco applied over metal lath or wire mesh. Edit to suit project requirements.

D.	Verify that [metal lath] [wire mesh] is tight, properly secured, and overlapped.

3.2	INSTALLATION OF METAL LATH

A.	Perform Work in accordance with ASTM C1063.

B.	Apply with long dimension perpendicular to supports, with end joints staggered.

C.	Lap ends minimum 1 inch and sides minimum 1-1/2 inches.

D.	Screw to framing at maximum 7 inches on center.

E.	Stop lath at each side of expansion and control joints and secure.

Include the following for polystyrene foam; edit to suit project requirements.

3.3	INSTALLATION OF POLYSTYRENE INSULATION

A.	Install with long joints continuous and end joints staggered.

B.	Secure to substrate with continuous beads of adhesive.

Edit the following to include only those metal trim profiles required for project; edit to suit project requirements.

3.4	INSTALLATION OF ACCESSORIES

A.	Install casing beads where stucco abuts dissimilar material or stops with edge exposed.

B.	Install corner beads at external corners.

C.	Install control joints

1.	Locate as follows unless otherwise indicated on Drawings:

a.	As required to limit each area of plaster to [144] [__] square feet with no dimension exceeding [12] [18] feet.

b.	Horizontally at each floor line.

2.	Run vertical joints continuous; butt horizontal joints into vertical joints.

3.	Apply joint sealer to form waterstop behind joints at intersections.

D.	Install expansion joints at locations indicated on Drawings.

E.	Install weep screeds at bottom of wall.

F.	Set level and true to line. [Wire tie to [metal lath] [wire mesh] at maximum 12 inches on center.] [Screw to supports at maximum [12] [__] inches on center.]

Edit the following to suit project requirements.

3.5	APPLICATION OF BASE COAT

A.	Apply base coat in accordance with ASTM C926 and manufacturer’s instructions.

B.	Apply to nominal 3/8 inch thickness from [face of lath.] [face of [concrete.] [masonry.]]

C.	Level surface to acceptable plane.

D.	Float surface to provide bond with finish coat.

**** OR ****

E.	Apply desired texture or pattern by doubling back and applying additional base coat material as soon as first coat is firm enough to prevent damage.

F.	Work from wet edges to apply unbroken area in one continuous operation to eliminate joints.

G.	Finish surfaces true to plane, plumb and with neat, sharp corners and intersections.

H.	Work in panels to nearest natural break formed by intersections, corners, trim, and accessories.

I.	Tool base coat to V-joint at trim, grounds and accessories.

Include the following for a Portland cement finish coat; edit to suit project requirements.

3.6	APPLICATION OF CEMENT-BASED FINISH COAT

A.	Apply finish coat in accordance with manufacturer’s instructions.

B.	Apply to minimum thickness recommended by manufacturer; using sufficient trowel pressure or spray velocity to bond finish coat to base coat.

C.	Apply in number of coats required to produce consistent finish.

D.	Provide [fine spray] [medium spray] [heavy spray] [smooth trowel] [____] texture to match approved mockup.

E.	Work from wet edges to apply unbroken area in one continuous operation to eliminate joints.

F.	Finish surfaces true to plane, plumb and with neat, sharp corners and intersections.

G.	Work in panels to nearest natural break formed by intersections, corners, trim, and accessories.

H.	Apply fog coat by brush, roller, or spray in number of coats required to produce consistent finish matching approved mockup.

I.	Allow fog coat to dry, then mist with water twice daily for 2 days.

Include the following for an acrylic or elastomeric finish coat; edit to suit project requirements.

3.7	APPLICATION OF [ACRYLIC] [ELASTOMERIC] FINISH COAT

A.	Apply primer and finish coat in accordance with manufacturer’s instructions.

B.	Apply in number of coats required to produce consistent finish.

C.	Provide [fine spray] [medium spray] [heavy spray] [rolled] [____] texture to match approved mockup.

D.	Work from wet edges to apply unbroken area in one continuous operation to eliminate joints.

E.	Finish surfaces true to plane, plumb and with neat, sharp corners and intersections.

F.	Work in panels to nearest natural break formed by intersections, corners, trim, and accessories.

Edit the following to suit project requirements.

3.8	CURING

A.	Moist cure Portland cement base coat in accordance with manufacturer’s instructions.

B.	Allow to air cure 10 to 14 days prior to applying [acrylic] [elastomeric] finish coat.

C.	[Do not wet cure acrylic or elastomeric finish coat.]

3.9	ADJUSTING

A.	Repair or replace damaged, discolored, and defective work.

B.	Blend patched areas to surrounding surfaces.

3.10	CLEANING

A.	Clean stucco from trim and accessories before initial set occurs.

END OF SECTION